## Slide 1
ERSI 904
Enjeux énergétiques, labels, réglementation et STD
Energy calculations, labels and regulations
Simon Rouchier

## Slide 2
<numéro>
Session | Day | Time
1 | 15/11/17 | 8h15
2 | 15/11/17 | 10h00
3 | 16/11/17 | 8h15
4 | 20/11/17 | 13h30
5 | 20/11/17 | 15h15
6 | 24/11/17 | 8h15
7 | 24/11/17 | 10h00
8 | 27/11/17 | 13h30
9 | 27/11/17 | 15h15
Bioclimatic houses Christophe Ménézo
Energy labels Mickaël Pailha
Heat transfer and HVAC calculations Simon Rouchier

## Slide 3
<numéro>
Building construction characteristics
Heating and cooling loads ; latent loads
1. Heat transfer calculations
2. Sizing HVAC systems
3. Humidity and AHUs
4. Control systems

## Slide 4
<numéro>
http://ebeclim.org

## Slide 5
<numéro>
Module | Lessons
1. Heat transfer in buildings | Electrical analogy
 | Thermal inertia
 | Thermal radiation
 | Air flow
2. HVAC systems | Heating networks
 | Domestic hot water
 | Ventilation and pressure
3. Humidity and AHU | The psychrometric chart
 | Air mixtures
 | Air handling units
4. Control systems | First order linear systems
 | PID controllers
Session | Day | Time
1 | 15/11/17 | 8h15
2 | 15/11/17 | 10h00
3 | 16/11/17 | 8h15
4 | 20/11/17 | 13h30
5 | 20/11/17 | 15h15
6 | 24/11/17 | 8h15
7 | 24/11/17 | 10h00
8 | 27/11/17 | 13h30
9 | 27/11/17 | 15h15

## Slide 6
<numéro>
Session | Day | Time | 
1 | 15/11/17 | 8h15 | Exercise 1
2 | 15/11/17 | 10h00 | 
3 | 16/11/17 | 8h15 | Exercice 2
4 | 20/11/17 | 13h30 | Exercise 3
5 | 20/11/17 | 15h15 | 
6 | 24/11/17 | 8h15 | Exercise 4
7 | 24/11/17 | 10h00 | 
8 | 27/11/17 | 13h30 | Test
9 | 27/11/17 | 15h15 | 

## Slide 7
<numéro>
Exercise 1
15/11/17
Solve the exercise on http://ebeclim.org/heat_inertia.html
Simulate the dynamic behaviour of this wall in the following conditions:
initial conditions T=10°C on the whole wall
for t>0 : Text = 2°C and Tint = 19°C
> draw the temperature at the concrete-insulation interface with respect to time

## Slide 8
<numéro>
Exercise 4 : project
20/11/17 and 24/11/17
Room 1
20 m2
48 m3
Component | Characteristics
External wall | Area : 31,2 m2 (room 1); 15,6 m2 (room 2) Transmittance : U= 0,45 W/m2.K
Window | Area : 2 m2 Transmittance : U= 2,9 W/m2.K Solar gain : 42%
Partition wall | Area : 12 m2 Transmittance : U= 11 W/m2.K
Ventilation rate | 1 vol/h
Room 2
10 m2
24 m3
Air flow direction
Find the heating power required to maintain 19°C in the room for an average outdoor temperature of 9°C
Simulate the transient temperature of room 1 and 2, using the outdoor temperature from the data file

## Slide 9
<numéro>